A Signal Processing Method for  Noise Evaluation Index Based on Quantized Levels

Yasuo Mitani†, Noboru Nakasako††, and Kazuhiro Tsutsumoto†††

mitani@fuee.fukuyama-u.ac.jp  nakasako@info.waka.kindai.ac.jp  tsutsu@fucc.fukuyama-u.ac.jp

†Faculty of Engineering, Fukuyama University, Hiroshima, 729-0292 Japan

††School of Biology-Oriented Science and Technology, Kinki University, Wakayama, 649-6492 Japan

†††Faculty of Human Cultures and Sciences, Fukuyama University, Hiroshima, 729-0292 Japan

Summary

The noise fluctuation is very often measured in a quantized level form at a discrete time interval.  By paying attention to this quantization procedure of the actual noise measurement, in this paper, a precise estimation method for the  noise evaluation index is proposed by using the roughly observed data with quantized levels.  That is, we first introduce theoretically a general statistical orthonormal expression of the probability density function for the original noise level fluctuation of continuous level type before passing through the level quantization measurement mechanism. Based on this quantization mechanism, we propose an estimation method of the distribution parameters in the above statistical expression by using the statistical information on the roughly observed data.  By using the estimated distribution parameters, we propose a signal processing method for estimating . The effectiveness of the proposed method is confirmed experimentally by applying it to first the simulation experiment and then the actual road traffic noise data.

Key words:

Signal processing method, Precise estimation of , Roughly observed data, Reduction of quantization errors

1. Introduction

When the statistical evaluation and/or prediction problems of a random noise environment are discussed, especially from the methodological viewpoint, the following points are essentially important :

(i)	As is well-known, the  noise evaluation index plays an important role in the field of noise evaluation and/or regulation problems [1].

(ii)	The environmental noises which we encounter in our daily life exhibit various types of probability distribution forms, apart from a standard Gaussian distribution, due to the diversified causes of fluctuation.

(iii)	In an actual observation, the noise fluctuation is very often measured in a quantized level form at a discrete time interval [2].

(iv)	In this case, it increases in importance, especially from a methodological viewpoint, to establish a unified statistical treatment for evaluating , and to develop a signal processing method for the reduction of level quantization errors.

(v) Moreover, when taking a fairly long term measurement, a reasonable estimation method from the roughly observed level data is very effective to reduce the memory capacity for computer processing.  As contrasted with this level quantization, it is necessary for the sufficient measurement accuracy to employ a suitably fine sampling interval [3],[4].

Based on these practical points of view, in this paper, a precise estimation method of  for the original noise level fluctuation of continuous level type before passing through the level quantization measurement mechanism.  That is, we first introduce theoretically a general statistical orthonormal expression of the probability density function for the original noise level fluctuation of continuous level type before passing through the level quantization measurement mechanism.  Next, based on the quantization error in this quantization mechanism, we propose an estimation method of the parameters in this statistical expression by using the statistical information on the roughly observed data with quantized levels.  On the basis of this estimation theory, an estimation method for the  noise evaluation index is proposed.

Finally, the principal effectiveness of the proposed method is experimentally confirmed by applying it to the simulation experiment.  And then, the practical effectiveness of the proposed method is experimentally confirmed by applying it to the actual road traffic noise data.

2. Theoretical Consideration

Let  be an original noise level fluctuation with an arbitrary probability density function of continuous level type before passing through a quantization measurement mechanism.  Also, let  be the quantized level value of  after passing through the quantization measurement mechanism, as shown in Fig. 1.  In this case, the mathematical relationship between  and  can be expressed by using the function form  of level quantization mechanism, as follows :

.                  (1)

In general, a level difference interval is set to be a fixed constant value .  Thus, by introducing integer number , the above relationship can be rewritten as :

.          (2)

Here, Eq.(1) can be rewritten by introducing the quantization error , as follows :

.                 (3)

Let us introduce the statistical Hermite expansion series expression, which is generally applicable to the arbitrary non-Gaussian distribution form, as the probability density function  of the original noise level fluctuation  before passing the above quantization mechanism, as follows [5] :

(4)

with       ,            (5)

Fig. 1 Quantization procedure for measurement of noise level fluctuation.

where  and  denote respectively the mean value of  and the standard deviation.  Moreover,  denotes an averaging operation with respect to the random variable  and  denotes the th order Hermite polynomial.  In addition,  denotes the expansion coefficient and  denotes the well-known Gaussian distribution defined as :

.         (6)

On the other hand, the relationship between the noise level fluctuation  and the noise intensity fluctuation  is given by :

,                (7)

where  denotes the reference noise intensity usually taken as .  After introducing the dimensionless ratio variable for the noise intensity fluctuation, i.e., , the probability density function  can be given after transforming  given by Eq.(4) into  based on the probabilistic measure preserving transformation, as follows :

,  (8)

where  is defined as :

.                 (9)

Based on Eq.(8), the mean value of  can be expressed as :

.    (10)

By substituting the mean value  given by Eq.(10) into the definition of , we can derive an evaluation method generally applicable to arbitrary noise level fluctuation with non-Gaussian distribution form, as follows :

.    (11)

This estimation formula agrees with the previous study [6] derived from another derivation process.  It should be noted that the above evaluation method agrees completely with the well-known usual evaluation method as a special case with the assumption of the standard Gaussian distribution, as follows [7] :

,       (12)

since the higher order expansion terms become zero for this case.  Thus, this estimation method takes a generalized form including the well-known simplified evaluation method as the first expansion term.

It is necessary to estimate the above distribution parameters ,  and  by using the quantized noise level data .  The mean value  of  and the variance  can be evaluated under the assumption of statistical independency between  and , as follows :

,                (13)

,                (14)

where  and  denote respectively the mean value of  and the variance.  By introducing the practical assumption of uniform distribution of  in the level quantization interval ,  and  can be given by :

,                 (15)

.                (16)

The expansion coefficient  with respect to  is expressed according to its definition, as follows :

.          (17)

This formula can be rewritten by substituting Eq.(3), Eq.(13) and Eq.(14) into Eq. (17), as follows :

.     (18)

Moreover, by paying attention to the statistical independency between  and , Eq.(18) can be rewritten based on the additive property of Hermite polynomial, as follows :

.    (19)

From Eq.(19), the expansion coefficient  can be derived by use of , as follows :

. (20)

From Eq.(20), the objective expansion coefficient  can be estimated based on  with the use of the statistics of .

It is possible to estimate the distribution parameters ,  and  by using the statistical information of the quantized noise level data , by using Eq.(13), Eq.(14) and Eq.(20).  Based on the estimated values of the distribution parameters, the objective evaluation index can be estimated after substituting them into Eq.(11).

3. Experimental Consideration

3.1 Simulation Experiment

In order to confirm the validity of the proposed method, it has been first applied to the simulation experiment.  In this simulation experiment, the random noise is generated by use of Gaussian random numbers.  The generated random noises have been roughly sampled at multiples of 5 dB quantized level difference with  by use of the following two procedures :

(i) Procedure 1.  Round off the random noise level  to quantized level  according to the following procedure :

.            (21)

(ii) Procedure 2.  Round down the random noise level  to quantized level  according to the following procedure :

,             (22)

where [ ] denotes a Gauss’ notation.

Because of the usage of Gaussian random numbers, it is sufficient to estimate only the mean value  and the standard deviation  in the proposed evaluation method.  And, the well-known estimation formula of Eq.(12) derived under the assumption of Gaussian distribution can be used in this simulation experiment.

Of course, it is impossible to evaluate precisely the experimental values of the objective  by using directly the roughly quantized level data.  For reference, in the following experimental results, these experimental values based on the direct evaluation from the quantized level data are shown in order to compare these direct values with the estimated values by using the proposed precise estimation method.

Table 1 shows the results for  estimated by use of the proposed method for the simulation data by procedure 1.  Moreover, the estimated results by procedure 2 are shown in Table 2.  According to these tables, the estimated values by using the proposed method are in good agreement with the experimental values.

Table 1: The estimated results forby using the proposed method

for the simulation data (procedure 1)

| Experimental value (dB) | Quantized level difference (dB) | Estimated results by use of the proposed method (dB) |
| --- | --- | --- |
|  |  | Direct evaluation from the quantized level data (dB) |
| 72.9 | 5 | 72.8 |
|  |  | 73.1 |
|  | 10 | 72.7 |
|  |  | 74.8 |
|  | 15 | 74.1 |
|  |  | 74.8 |
|  | 20 | 75.4 |
|  |  | 76.1 |

Table 2: The estimated results forby using the proposed method

for the simulation data (procedure 2)

| Experimental value (dB) | Quantized level difference (dB) | Estimated results by use of the proposed method (dB) |
| --- | --- | --- |
|  |  | Direct evaluation from the quantized level data (dB) |
| 72.9 | 5 | 72.7 |
|  |  | 70.9 |
|  | 10 | 72.6 |
|  |  | 68.2 |
|  | 15 | 72.4 |
|  |  | 67.0 |
|  | 20 | 72.3 |
|  |  | 65.2 |

3.2 Application to Road Traffic Noise Data

In this section, we have applied the proposed method to the actual road traffic noise data with non-Gaussian property in order to confirm the practical effectiveness of the proposed method.  The road traffic noise data have been measured in Fukuyama City by use of a precision sound level meter.  In order to evaluate precisely and directly the experimental values of , the A-weighted noise level fluctuation with a fine level quantization interval of 0.1 dB has been measured at a fine sampling time interval of 0.2 sec.  The total measuring time interval has been selected as 10 minutes.  An arrangement of the noise measurement is shown in Fig. 2.  As shown in the simulation experiment, the measured level data of road traffic noise have been also quantized at multiples of 5 dB level difference interval with  by use of the same two level quantization procedures.

Table 3 shows the estimated results for  by using the proposed method for level data with a same quantized level difference of 10 dB (by procedure 1). Furthermore, Table 4 shows the results for  estimated by use of the proposed method for the same data by procedure 2.  According to these tables, the estimated values by using the proposed method are in good agreement with the experimental values.

Fig. 2  The arrangement of the noise measurement.

Table 3: The estimated results forby using the proposed method

for road traffic noise data (procedure 1)

| Experimental value (dB) | Direct evaluation from quantized level data (dB) | Estimated results by use of the proposed method (dB) |
| --- | --- | --- |
| 65.7 | 66.7 | 64.4 (First term) |
|  |  | 66.5 (First approx.) |
|  |  | 66.3 (Second approx.) |
|  |  | 65.6 (Third approx.) |

Table 4: The estimated results forby using the proposed method

for road traffic noise data (procedure 2)

| Experimental value (dB) | Direct evaluation from quantized level data (dB) | Estimated results by use of the proposed method (dB) |
| --- | --- | --- |
| 65.7 | 61.7 | 64.3 (First term) |
|  |  | 65.5 (First approx.) |
|  |  | 65.4 (Second approx.) |
|  |  | 65.6 (Third approx.) |

4. Conclusion

In an actual observation, the noise fluctuation is very often measured in a quantized level form at a discrete time interval.  In this case, it increases in importance, especially from a methodological viewpoint, to establish a unified statistical treatment for evaluating the  noise evaluation index, and to develop a signal processing method for the reduction of level quantization errors.

The main point of this study is how to establish a new statistical evaluation method for environmental noise by considering the level quantization mechanism of the environmental noise measurement.  First, we have introduced a general statistical orthonormal expression of the probability density function for the original noise level fluctuation of continuous level type before passing through this quantization measurement mechanism.  Next, based on the level quantization mechanism, we have proposed a reasonable estimation method of the distribution parameters in the above statistical expression by using the statistical information on the roughly observed data with quantized levels.  On the basis of this estimation theory, a precise evaluation method for thenoise evaluation index has been proposed.  This precise estimation method is effective for a fairly long term measurement.

Finally, the principal effectiveness of the proposed method has been confirmed experimentally by applying it to the simulation experiment.  Furthermore, the practical effectiveness of the proposed method has been experimentally confirmed by applying it to the actual road traffic noise data measured in Fukuyama City.

This research is at an early stage of study.  There still remain several problems to be solved in future such as :

(i)	applying the proposed method to various kinds of data in many actual environmental noises,

(ii)	finding a reasonable method to determine an optimal order of series expansion in the proposed estimation method.

## Acknowledgment

The authors would like to express their cordial thanks to Dr. Mitsuo Ohta for his valuable advice.

References

[1] C. M. Harris, Handbook of Noise Control, McGraw-Hill, New York, 1978.

[2] M. Ohta, S. Yamaguchi and Y. Mitani, “A new on-line estimation method of representative statistics of environmental random noise and vibration based on actual digital measurement,” J. Acoust. Soc. Jpn. (J), vol.39, pp.361-366, 1983 (in Japanese).

[3] D. J. Fisk, “Statistical sampling in community noise measurement,” J. Sound Vib., vol.30, pp.221-236 (1973).

[4] J. G. Vaskor, S. M. Dickinson and J. S. Bradley,  “Effect of sampling on the statistical descriptors of traffic noise,”  Appl. Acoust., vol.12, pp.111-124, 1979.

[5] M. Ohta and T. Koizumi, “General statistical treatment of response of a linear rectifying device to a stationary random input,” IEEE Trans. Inf. Theory, vol.IT-14, pp.595-598, 1968.

[6] Y. Mitani, M. Ohta and Y. Xiao, “A new estimation method of noise evaluation index,, by use of the statistical information on the arbitrary type noise level fluctuation,” J. Acoust. Soc. Jpn. (E), vol.9, pp.47-51, 1988.

[7] U.S. Environmental Projection Agency, “Information on levels of environmental noise requisite to protect public health and welfare with an adequate margin of safety,” 550/9-74-004, 1974.

Yasuo Mitani    received the B.E. and M.E. degrees, from Fukuyama Univ. in 1979 and 1981, respectively.  He received the Dr. Eng. degree from Hiroshima Univ. in 1990.  After working as a research assistant  (from 1983), an assistant professor (from 1991) in the Dept. of Electronic and Electrical Engineering, Fukuyama Univ., and an associate professor (from 1996), he has been a professor at Fukuyama Univ. since 2000. His research interest includes acoustic signal processing, sound and vibration control, and their application to acoustics.  He is a member of ASJ, IEICE, SICE, ISCIE, and INCE Japan.

Noboru Nakasako    received the B.E., M. E., and Dr. Eng. degrees from Hiroshima Univ. in 1982, 1984, and 1990, respectively.  After working as a research assistant (from 1986), an assistant professor (from 1990) in the Dept. of Electrical Engineering, the Hiroshima Institute of Technology, and an associate professor (from 1994) in the Faculty of Biology-Oriented Science and Technology, Kinki Univ., he has been a professor at Kinki Univ. since 2002. His research interest includes acoustic signal processing, sound and vibration control, independent component analysis and their application to acoustics.  He is a member of ASJ, IEICE, SICE, ISCIE, and INCE Japan.

Kazuhiro Tsutsumoto   received the B.E. degree from Fukuyama Univ. in 1979. After working as a research assistant (from 1979), and an assistant professor (from 1993) in the Faculty of Liberal Arts, Fukuyama Univ., he has been an associate professor at Fukuyama Univ. since 2001. His research interest includes acoustic signal processing, sound and vibration control, and their application to acoustics.  He is a member of SICE, IPSJ, JSISE, and JSEI.